## Slide 1: Implementation and Evaluation of Pseudo LRU cache eviction policy
Shubhojit Chattopadhyay
CS7290, Spring 2012

## Slide 2: Why cache eviction?
Caches have limited capacity
Set Associative caches have have conflict misses (Index is same but Tag is different)
How to decide which way to evict?
Way A
Memory access address
Cache
Tag A
Index
Each way = one cache line (64B)
Way B
Tag B
Way C
Tag C
Way D
Tag D

## Slide 3: Commonly used policies
Random
Most Recently used (keep track of which way was the one last used)
FIFO
Least Recently used
Not Recently Used

## Slide 4: Random Policy
Way A
Way B
Way C
Way D
Way A
Way B
Way C
Way D
Way A
Way E
Way C
Way D
Way A
Way E
Way L
Way D
Initial State
Access B
Access E
Access L
1
0
0
Linear Feedback shift register
0
Pseudo Random generates 01
Pseudo Random generates 10
Evict Way B
Evict Way C
No effect

## Slide 5: FIFO Policy
Way A
Way B
Way C
Way D
Way A
Way B
Way C
Way D
Way E
Way A
Way B
Way C
Way L
Way E
Way A
Way B
Initial State
Access B
Access E
Access L
Last In
First In
No effect
Evict Way D
Evict Way C

## Slide 6: LRU Policy
Way A
Way B
Way C
Way D
Way B
Way A
Way C
Way D
Way E
Way B
Way A
Way C
Way L
Way E
Way B
Way A
Initial State
Access B
Access E
Access L
Most recently used
Least recently used
Update location of B
Evict Way D
Evict Way C

## Slide 7: Need for a new policy
Primary disadvantage of above policies
  Some have high eviction rate
  Some have Hardware and latency concerns
  Some have higher Energy Concerns
  How to maintain small latencies for closest caches if we have to update so much?
Problems with True LRU
  Expensive in terms of speed and hardware
  Need to remember the order in which all N lines were last accessed
  N! scenarios  O(N log N) LRU bits
    2-ways  AB BA = 2 = 2!
    3-ways  ABC ACB BAC BCA CAB CBA = 6 = 3!

## Slide 8: Pseudo – LRU policy
Tree based tracking
Not exactly LRU, but not far from it either
O(N) number of bits
Faster than LRU

## Slide 9: Pseudo LRU
AB/CD bit (L0)
A/B bit (L1)
C/D bit (L2)
Way A
Way B
Way C
Way D
A
B
C
D
Way0
Way1
Way2
Way3
Tree-based
O(N): 3 bits for 4-way
Cache ways are the leaves of the tree
Combine ways as we proceed towards the root of the tree

## Slide 10: How it works
L2 | L1 | L0 | Way to replace
X | 0 | 0 | Way A
X | 1 | 0 | Way B
0 | X | 1 | Way C
1 | X | 1 | Way D
Way hit | L2 | L1 | L0
Way A | --- | 1 | 1
Way B | --- | 0 | 1
Way C | 1 | --- | 0
Way D | 0 | --- | 0
LRU update algorithm
Replacement Decision
AB/CD bit (L0)
A/B bit (L1)
C/D bit (L2)
Way A
Way B
Way C
Way D
AB/CD
AB
CD
AB/CD
AB
CD
L2L1L0 = 000,
there is a hit in Way B, what is the new updated L2L1L0?
L2L1L0 = 001,
a way needs to be replaced, which way would be chosen?
0
0
0
1
1
1

## Slide 11: Implementation in Simplescalar
All cache policies are a case in cache.c. Caches are a set of structs that are chained in a queue
Create another case for plru. Each cache set has it’s own plru vector
For each access, check if it is a hit or a miss
If Hit,
  Update the plru vector based on the tree (vector = L2L1L0)
  Getvector (current_vector, num_of_ways, hit_way)
If Miss,
  Find the Least recently used way using the current plru vector
  Evictway(current_way, num_of_ways)
  Getvector() to update the plru vector now since this is most recently used way now

## Slide 12: Performance Evaluation
Baseline Cache configuration for evaluation (unless otherwise specified):
  Intel Clarkdale Microarchitecture (1st gen Core i3)
  Split L1 Instruction and Data Cache (32KB, 8 ways)
  Unified L2 cache (256KB, 8 ways)
Testing methodology
  Modify config file to activate different policies
  Run the simulator through SPEC2000 benchmarks for 10 million instructions
Performance Metrics:
  Replacement/Eviction Rate
  IPC
  Power Consumption
  Storage/Hardware update requirements per cache access

## Slide 13: Performance Evaluation(Replacement Rate)
Replacement Rate for policies in L1 cache:
  LRU only slightly better than plru
  Plru, however, performs better than random or FIFO

## Slide 14: Performance evaluation (Replacement Rate)
Replacement rate for pLRU with increasing number of ways (overall L1 cache size =32KB const)

## Slide 15: Performance evaluation (IPC)
IPC with increasing L1 cache size
  IPC of pLRU is only slightly worse than LRU in all cases, with Random in 3rd and FIFO is the worst

## Slide 16: Performance Evaluation (IPC)
IPC when plru is used in both L1 and L2 as opposed to using only in one level
  Higher IPC when used only in L2 (because L1 has LRU)
  Using in both levels makes IPC performance even worse

## Slide 17: Performance Evaluation (Power)
Power Consumption is calculated using CACTI simulator (provided by HP)
Takes various cache configurations as input and the computes Dynamic Read energy consumption, area and complexity
Inputs like Cache line size, technology node etc.
Has a web interface, but for most purposes you need to download the source

## Slide 18: Energy consumption calculation
For the clarkdale configuration (L1 32KB and 8 ways, L2 256KB and 8 ways)
Total energy consumption = Total Energy consumed in all accesses in L1 + Total energy consumed in all accesses in L2
In the above formula, Energy consumed in each level of cache = Dynamic read energy per access*Total number of accesses in that cache level
where Dynamic read energy/access = Dynamic read energy of Data array/per access + Dynamic read energy of Tag/access

## Slide 19: Performance Evaluation (Energy)
So, we can see that plru overall consumes slightly more energy as compared to lru on account of more replacements. However the difference in energy consumption for 10 million cycles is very little.

## Slide 20: Performance Evaluation (Storage)
On every cache access, we need to update the tracking bits based on eviction policy

## Slide 21: Performance Evaluation (Storage)
For the same Intel clarkdale configuration

## Slide 22: Conclusion
pLRU is almost equivalent to LRU in terms of Eviction Rate, IPC and hit based energy consumption
The storage/update requirements for pLRU is lesser than LRU for almost the same IPC performance
Ideal for L1 caches

## Slide 23: References
[1] Ackland B., Anesko D., Brinthaupt D., DaubertS.J, Kalavade A.., Knoblock J., Micca E., Moturi M.,Nicol C.J., O’Neill J.H., Othmer J., Sackinger E.,Singh K. J., Sweet J., Terman C. J., and Williams J.,“A Single-Chip, 1.6 Billion, 16-b MAC/s Multiprocessor DSP,” IEEE Journal of Solid-state circuits, Vol. 35, No. 3, March 2000, pp. 412-423.
[2] Belady, L.A., “A study of replacement algorithms for a virtual storage computer,” IBM Systems Journal, 5(2):79- 101, 1966.
[3] Burger D., Austin T., “The SimpleScalar Tool Set, Version 2.0,” University of Wisconsin-Madison Technical Report #1342, June 1997.
[4] Cantin J. F, Hill M. D., Cache Performance of the SPEC CPU2000 Benchmarks, http://www.cs.wisc.edu/multifacet/misc/spec2000cach e- data/
[5]Hennessy J. L., Patterson D., Computer Architecture: A Quantitative Approach, Third Edition, Morgan Kaufmann Publishers, 2003.
[6] Henning J. L., SPEC CPU2000: Measuring CPU Performance in the New Millennium, IEEE Computer, vol. 33, no. 7, July 2000, pp. 28-35, http://www.spec.org/osg/cpu2000/papers/COMPUTE R_20 0007- bstract.JLH.html
[7] Wong W., Baer J-L., “Modified LRU Policies for Improving Second-level Cache Behavior,” Proceedings of the 6th International Symposium on High-Performance Computer Architecture, Toulouse, France, January 2000
[8] Hussein Al-zoubi, Ar Milenkovic, Milena Milenkovic, “Performance Evaluation of Cache Replacement Policies for the SPEC CPU2000 Benchmark Suite ”
[9] Hsin-Hsien Lee, class notes ECE 6100, Georgia Institute of Technology
[10] http://etd.nd.edu/ETD-db/theses/available/etd- 07122008-005947/unrestricted/ThoziyoorS072008.pdf for computation of dynamic power using CACTI
[11] http://www.hpl.hp.com/research/cacti/ HP Cacti simulator